The Stockholm Water Prize
GPS
NMEA Protocol

---
NMEA standard for GPS
- NMEA
  - National Marine Electronics Association
- GPS sentences standard
  - Self-reliant sentence
  - Independent from other sentences
  - Starts with ‘$’ sign, has ~80 characters
  - Ends with checksum + carriage return
http://www.engineersgarage.com/tutorials/gps-receivers-nmea-standards

---
More details on sentences
- ASCII text
- Varies in precision
- Checksum starts with '*'+2 hexadecimals
  - 8 bit exclusive OR of all the characters between $ and *
  - Not including, the $ and *
http://www.engineersgarage.com/tutorials/gps-receivers-nmea-standards

---
Connecting a GPS to Arduino
http://playground.arduino.cc/Tutorials/GPS
A GPS connects with Null-Modem:	- 4800 bps, 8 bits, 1 stop bit
- no parity, no handshake

---
Sentences types
$GPGGA:
  - Global Positioning System Fix Data
$GPGSV:
  - GPS satellites in view
$GPGSA:
  - GPS DOP and active satellites
$GPRMC:
  - Recommended minimum specific GPS/Transit data
http://playground.arduino.cc/Tutorials/GPS

---
Detailing GPRMC sentence
- $GPRMC,225446,A,4916.45,N,12311.12,W,000.5,054.7,191194,020.3,E*68
  - 225446 Time of fix 22:54:46 UTC
  - A Navigation receiver warning A = Valid position, V = Warning
  - 4916.45,N Latitude 49 deg. 16.45 min. North
  - 12311.12,W Longitude 123 deg. 11.12 min. West
  - 000.5 Speed over ground, Knots
  - 054.7 Course Made Good, degrees true
  - 191194 UTC Date of fix, 19 November 1994
  - 020.3,E Magnetic variation, 20.3 deg. East
  - *68 mandatory checksum
http://playground.arduino.cc/Tutorials/GPS

---
Parsing NMEA stream
- $GPGGA,154654,4428.2011,N,00440.5161,W,0,00,,-00044.7,M,051.6,M,,*6B
- $GPGSA,A,1,,,,,,,,,,,,,,,*1E
- $GPGSV,3,1,10,02,50,290,00
- $GPGGA,154655,4328.1874,N,00340.5185,W,1,03,08.5,-00044.7,M,051.6,M,,*79
- $GPGSA,A,2,13,23,25,,,,,,,,,,08.5,08.5,00.9*0E
- $GPGSV,3,1,10,02,50,290,26,04,60,210,26,08,33,173,29,10,21,296,00*7E
- $GPGSV,3,2,10,13,58,044,34,16,03,035,00,20,02,109,00,23,26,057,34*7B
- $GPGSV,3,3,10,25,24,045,35,27,56,145,27,,,,,,,,*7D
- $GPRMC,154655,A,4428.1874,N,00440.5185,W,000.7,000.0,050407,,,A*6C
Not working yet
Time in UTC (HhMmSs): 154655
Status (A=OK,V=KO): A
Latitude: 4428.1874
Direction (N/S): N
Longitude: 00440.5185
Direction (E/W): W
Speed in Knots: 000.7
Heading in degrees: 000.0
Date in UTC (DdMmAa): 050407
Magnetic variation:
Variation (E/W):
Mode: A

---
Where is this GPS?
http://quaxio.com/arduino_gps/
- $GPGGA,004235.776,3746.2757,N,12223.3240,W,1,07,1.1,27.3,M,-25.3,M,,0000*54
- $GPGSA,A,3,02,04,24,28,09,17,15,,,,,,2.0,1.1,1.6*36
- $GPGSV,3,1,12,04,57,134,35,24,56,287,36,05,55,318,,17,41,046,32*7C
- $GPGSV,3,2,12,02,39,177,24,12,31,305,26,28,17,099,36,30,14,297,*74
- $GPGSV,3,3,12,09,10,157,31,15,10,234,36,20,,044,,48,44,197,37*73
- $GPRMC,004235.776,A,3746.2757,N,12223.3240,W,0.22,173.75,170613,,,A*7B
- $GPGGA,004236.776,3746.2770,N,12223.3217,W,1,07,1.1,39.9,M,-25.3,M,,0000*55
- $GPGSA,A,3,02,04,24,28,09,17,15,,,,,,2.0,1.1,1.6*36
- $GPRMC,004236.776,A,3746.2770,N,12223.3217,W,0.13,211.41,170613,,,A*7D
- $GPGGA,004237.776,3746.2779,N,12223.3198,W,1,07,1.2,50.6,M,-25.3,M,,0000*5A
- $GPGSA,A,3,02,04,24,28,09,17,15,,,,,,2.0,1.2,1.6*35
- $GPRMC,004237.776,A,3746.2779,N,12223.3198,W,0.16,173.46,170613,,,A*74
Use Google Maps/Earth to display the result
Was it later or earlier than the previous NMEA stream?

---
Answer 1
- 3746.2779,N,12223.3198,W
  - Lat: 37+(46.2779/60) = 37.7713
  - Lon: -1*(122+(23.3198/60)) = -122.3887
http://quaxio.com/arduino_gps/

---
Answer 2
...

---
End