Change Detection Addendum

Note on the extension of the total change of magnitude per pixel from spatial-diachronic to spectro-temporal. CM expresses the land use continuum as per the classes mean value temporal distances.

It should be noted that standard CM (spatial-diachronic) would be:

CM_{pixel}= sum from{k=1} to{n} sqrt{left[ B_{k,t+1} - B_{k,t} right]^2}	(1)

If we consider more than two images spectral bands in time, a direct extension of CM becomes:

CM_{ST}= sum from{t=0} to{T} sum from{s=0} to{S} sqrt{left[ B_{t+1,s} - B_{t,s} right]^2}	(2)

where it is clear that:
t is a part of the full time T
S is the total image spectral bands
s is an image band (from 1 pixel to S)

This assumes that the images Bands (B) are of different spectral definitions.